## Slide 1: Basic Ultrasound Physics
ACSES Sabah 2009

## Slide 2: Basic Ultrasound Physics
Sound
  mechanical wave, which requires a medium in which to travel.
  It is a series of pressure waves propagating through a medium.
  Transfer of energy through medium
One cycle of the acoustic wave
  composed of a complete positive and negative pressure change.
  The wavelength is the distance traveled during one cycle,
  The frequency of the wave is measured in cycles per second or Hertz (Cycles/s, Hz,
ACSES Sabah 2009

## Slide 3: Basic Ultrasound Physics
For humans audible sound ranges between 16 Hz and 20.000 Hz (20 kHz).
The hearing range of other species can be much higher than 20 kHz and is inaudible for us.
These higher wave frequencies are referred to as “ultrasound”
ACSES Sabah 2009

## Slide 4: Basic Ultrasound Physics
The speed acoustic wave travels through a medium is determined by the density and stiffness of the medium.
> stiffness, the faster the wave will travel.
Acoustic waves are calculated to travel through human tissue at body temperature at approximately 1540 m/s
When traveling through a medium the sound waves' intensity and amplitude decreases. This is called 'attenuation' and is the reason why echoes from deeper structures are weaker than echoes from superficial areas.
Other mechanisms are reflection, refraction and scatter.
ACSES Sabah 2009

## Slide 5: Basic Ultrasound Physics
The production of ultrasound waves is based on the so-called ‘pulse echo' principle.
The source of the ultrasound wave is the piezoelectric crystal, which is placed in the transducer. This crystal has the ability to transform an electrical current into mechanical pressure waves (ultrasound waves) and vice versa.
Once the ultrasound wave is generated and travels through the medium, the crystal switches from ‘sending’ into ‘listening’ mode and awaits returning ultrasound echoes. Actually, over 99% of the time is spent 'listening'. This cycle is repeated several million times per second.
This principle is called 'pulse echo'≠ principle. Returning sound waves are converted into images on the ultrasound monitor
ACSES Sabah 2009

## Slide 6: Basic Ultrasound Physics
Diagnostic ultrasound used for common medical imaging uses frequencies between 2 and 20 MHz. Lower frequencies are able to penetrate deeper into tissue but show poorer resolution. On the other hand, higher frequency ultrasound will display more detail with a higher resolution in exchange for less depth penetration.
This trade-off between resolution and penetration
  Very important principle when choosing your probes and frequencies
ACSES Sabah 2009

## Slide 7: Ultrasound Modes
ACSES Sabah 2009

## Slide 8: II. Ultrasound Modes
The most important mode for the ultrasound-beginner is the B-mode.
B-mode stands for ‘brightness mode’ and provides structural information utilizing different shades of gray (or different ‘brightness’) in a two-dimensional image
ACSES Sabah 2009

## Slide 9: II. Ultrasound Modes
M-mode stands for ‘motion mode’. It captures returning echoes in only one line of the B-mode image but displays them over a time axis.
Movement of structures positioned in that line can now be visualized. Often M-mode and B-mode are displayed together on the ultrasound monitor
ACSES Sabah 2009

## Slide 10: II. Ultrasound Modes
The Doppler mode follows very sophisticated and complex laws of physics.
Phenomenon called ‘Doppler shift’, which is a change in frequency from the sent to the returning sound wave. These changes or ‘shifts’ are generated by sound waves reaching moving particles.
The change of frequency/amount of shift correlates with the velocity and direction of particle motion. In simplified terms, the Doppler mode examines the characteristics of direction and speed of tissue motion and blood flow and presents it in audible, color or spectral displays
ACSES Sabah 2009

## Slide 11: II. Ultrasound Modes
Color Doppler ultrasound is also called 'color-flow ultrasound'. It is able to show blood flow or tissue motion in a selected two-dimensional area.
Direction and velocity of tissue motion and blood flow are color coded and superimposed on the corresponding B-mode image
ACSES Sabah 2009

## Slide 12: II. Ultrasound Modes
Power Doppler: Unlike color Doppler, common power Doppler does not examine flow velocity or the direction of flow. It looks at the amplitudes of the returning frequency shifts and is able to detect even states of very low flow
This is of use when evaluating vascular emergencies such as testicular or ovarian torsion.
ACSES Sabah 2009

## Slide 13: II. Ultrasound Modes
Spectral Doppler consists of a continuous and pulsed-wave form.
Continuous wave Doppler is often available as a separate small hand-held unit containing discrete transmitting and receiving piezo-electric crystals. This allows for simultaneous transmitting of ultrasound waves and receiving of returning Doppler shift signals, which are converted to audible frequencies over a loudspeaker. No image is produced.
To demonstrate patent vessels or fetal heart tones in pregnancy. Pulsed-wave spectral Doppler shows the “spectrum” of the returned Doppler frequencies in a characteristic two-dimensional display.
ACSES Sabah 2009

## Slide 14: Artifacts
ACSES Sabah 2009

## Slide 15: III. Artifacts
Artifacts
  findings seen on the ultrasound image that do not exist in reality.
  can be helpful when interpreting the image or it can confuse the examiner.
ACSES Sabah 2009

## Slide 16: III. Artifacts:Attenuation Artifacts
Shadowing:
  caused by partial or total reflection or absorption of the sound energy.
  Weaker signal returns from behind a strong reflector (air) or sound-absorbing structure (gallstone, kidney stone, bone, figure
ACSES Sabah 2009

## Slide 17: III. Artifacts
Posterior Enhancement:
Area behind an echo-weak or echo-free structure appears brighter (more echogenic) than its surrounding structures.
This occurs because neighboring signals had to pass through more attenuating structures and return with weaker echoes
ACSES Sabah 2009

## Slide 18: III. Artifacts
Edge Shadowing:
The lateral edge shadow is a thin acoustic shadow that appears behind edges of cystic structures.
Sound waves encountering a cystic wall or a curved surface at a tangential angle are scattered and refracted, leading to energy loss and the formation of a shadow
ACSES Sabah 2009

## Slide 19: III. Artifacts :Propagation Artifacts
Reverberation:
Occurs when sound encounters two highly reflective layers. The sound is bounced back and forth between the two layers before traveling back.
The probe will detect a prolonged traveling time and assume a longer traveling distance and display additional ‘reverberated’ images in a deeper tissue layer
ACSES Sabah 2009

## Slide 20: III. Artifacts :Propagation Artifacts
Comet Tail:
Similar to reverberation. Produced by the front and back of a very strong reflector (air bubble, BB gun pellet).
The reverberations are spaced very narrowly and blend into a small band
ACSES Sabah 2009

## Slide 21: III. Artifacts :Propagation Artifacts
Mirror Imaging: If a structure is located close to a highly reflective interface (such as the diaphragm), it is detected and displayed in its normal position. However, the strong reflector causes additional sound waves to bend towards the neighboring anatomy, from where they are bounced back towards the strong reflector and return to the transducer.
These sound waves have a longer travel time and are perceived as an additional anatomic structure. The image is duplicated on the other side of the strong reflector
ACSES Sabah 2009

## Slide 22: III. Artifacts Miscellaneous Artifacts
Ring Down: Caused by a resonance phenomenon from a collection of gas bubbles. A continuous emission of sound occurs from the ‘resonating’ structure causing a long and uninterrupted echo.
Appears very similar to the comet tail artifact
ACSES Sabah 2009

## Slide 23: III. Artifacts Miscellaneous Artifacts:
Side Lobe: Caused by low energy ‘side lobes’ of the main ultrasound beam. When an echo from such a side lobe beam becomes strong enough and returns to the receiver, it is ‘assigned’ to the main beam and displayed at a false location. Side-lobe artifacts are usually seen in hypoechoic or echo-free structures and appear as bright and rounded lines
ACSES Sabah 2009

## Slide 24: Probes
ACSES Sabah 2009

## Slide 25: IV. Probes
Different types of probes are commonly used in emergency departments.
These transducers consist of the active element, damping material and a matching layer.
Different arrangements and forms of activation of the active element have lead to a variety of probes
ACSES Sabah 2009

## Slide 26: Common Terminology
ACSES Sabah 2009

## Slide 27: V. Common Terminology
**The beginner needs to be familiar with a few commonly used terms:
ACSES Sabah 2009

## Slide 28: V. Common Terminology
Image Interpretation:
Anechoic / Echolucent; Complete absence of returning sound waves, area is black.
Hypoechoic;
Structure has very few echoes and appears darker than surrounding tissue.
Hyperechoic / Echogenic; Opposite of hypoechoic, structure appears brighter than surrounding tissue.
ACSES Sabah 2009

## Slide 29: V. Common Terminology
Image Acquisition / Probe Positions:
Transverse Plane
Axial plane or cross section, separates the superior from the inferior, or, the head from the feet.
Sagittal Plane
Oriented perpendicular to the ground, separating left from right. The "midsagittal plane" is a sagittal plane that is exactly in the middle of the body.
Coronal Plane
Also known as the frontal plane, separates the anterior from the posterior or the front from the back.
Oblique Plane - The probe is oriented neither parallel to, nor at right angles from, coronal, sagittal or transverse planes.
Longitudinal Plane - The longitudinal plane is perpendicular to the transverse plane an can be either the coronal plane or sagittal plane.

## Slide 30: Knobology
ACSES Sabah 2009

## Slide 31: VI. Your Machine Functions
This section lists several important machine functions. They are more or less universal to all ultrasound equipment.
Information is kept as general as possible to make it applicable to most machines. Make every effort to be as familiar as possible with most of these functions.
On / Off - Remember how to switch the machine on before going into the patient’s room! Select / Change Probes - Select a specific probe. Set - Press to select from an activated menu; press to select/fixate a measurement point.
ACSES Sabah 2009

## Slide 32: VI. Your Machine Functions
Preset Menu
Select from preset menus such as general abdominal / vascular / procedures / OB or others. Use the scroll ball to navigate the menu. Scroll
Use the scroll ball (or in some machines a touch pad) to move the curser within the image or navigate through menus. After freezing an image-moving the scroll ball will display the last few images just before you pushed the freeze button (these images are called cine-loops) Gain
Changes overall strength of returning echoes, functions as an amplifier. TGC
Changes strength of returning echoes in a certain depth. Depth Adjustment
Increases or decreases the depth of the ultrasound beam. Freeze
Push to freeze the current image.

## Slide 33: VI. Your Machine Functions
Print / Save;
Print a frozen image and/or save an image to a hard drive. Measurement / Cursor ;
After activating the first measurement button, a marker will appear on the screen. Use the scroll ball (or sometimes this is a touch pad) to place it over the desired area. By pushing ‘set’ or ‘mark’ - the first cursor will be placed there and second cursor will appear. Use the scroll ball and the set button to complete the process. Additional measurements can be obtained by pushing the cursor button again. Some machines will have extra measurement buttons. Change Mode
Pushing the 'M-mode' button will change the machine to M-mode, 'Doppler' button to Doppler mode, 'color Doppler' to color, etc. Most machines are set up so that a 'dual' screen appears when certain modes are selected (B-Mode combined with Doppler or M-Mode etc.; see figure 2 and 5 as examples). Focus
Will change or add focal zones to the image
ACSES Sabah 2009

## Slide 34: Enjoy The Session… Good Luck
ACSES Sabah 2009